## Slide 1: Bank Alarm System & Highway Lights
By Batch 1
Abubaqar Mulla – 11
Aditya Chavan – 12
Aman Mulla – 20
Ashley Fernandez - 33

## Slide 2: Objectives
Bank Alarm System:
Objective: Enhance security by detecting suspicious activities and alerting security personnel.
Objective: Cost-effective system that provides value for money.
Highway Lights:
Objective: Improve road safety by providing adequate illumination on highways and roads.
Objective: Energy-efficient lights that reduce energy costs.

## Slide 3: Theory
Bank Alarm System:
A bank alarm system is a security system designed to protect a bank's premises and assets from theft, burglary, or any other security breaches. In an IoT-enabled bank alarm system, sensors and cameras are used to detect and monitor suspicious activities in real-time. The system is designed to alert security personnel or authorities immediately if it detects any security breaches. It can also be integrated with other security systems such as CCTV cameras, access control systems, and fire alarms to provide a comprehensive security solution.
Highway Lights:
Highway lights are an essential component of road safety, providing illumination to drivers and ensuring that they can see the road ahead clearly. In an IoT-enabled highway lights system, sensors and control systems are used to automatically adjust the lights' brightness and intensity based on the time of day, weather conditions, and traffic volume. This helps to ensure that the lights are always functioning optimally and providing the required illumination while minimizing energy consumption. The system can also be integrated with other IoT systems such as traffic management systems and weather monitoring systems to provide a comprehensive solution for road safety and efficiency.

## Slide 4: Algorithm
Highway Lights algorithm-
Initialize the pins for the liquid crystal display, light sensor, ultrasonic sensor, and LED.
Setup the liquid crystal display and serial communication.
Enter the loop function.
Read the value of the light sensor and display it on the first line of the LCD.
Trigger the ultrasonic sensor to measure the distance to an obstacle and display it on the second line of the LCD.
If the light sensor value is low and the distance measured by the ultrasonic sensor is less than or equal to 50 cm, turn on the LED for 5 seconds.
Otherwise, turn off the LED.
Clear the LCD and repeat the loop.

## Slide 5: Algorithm
Bank Alarm System algorithm-
Initialize the pins for the light sensor, ultrasonic sensor, gas sensor, and alarm.
Set the alarm pin to output mode and turn it off.
Start serial communication.
Enter the loop function.
Read the values of the light sensor, ultrasonic sensor, and gas sensor.
Check if the distance measured by the ultrasonic sensor is less than 20 cm and the gas value is greater than 250. If yes, turn on the alarm for 5 seconds and turn it off for 1 second.
Check if the light value is less than 100 and the distance measured by the ultrasonic sensor is less than 20 cm. If yes, turn on the alarm for 5 seconds and turn it off for 1 second.
Check if the distance measured by the ultrasonic sensor is less than 20 cm and the gas value is greater than 250. If yes, turn on the alarm for 5 seconds and turn it off for 1 second.
Print the values of the distance, light sensor, and gas sensor on the serial monitor.
Delay for 100 milliseconds and repeat the loop.

## Slide 6: Highway Lights code
#include<LiquidCrystal.h>
int LS=1;
int trig=6,echo=7;
int l1=A2,l2=A3;
int rs=16, en=17, d4=13, d5=12, d6=11,d7=10;
LiquidCrystal lcd(rs,en,d4,d5,d6,d7);
void setup() {
pinMode(l2,OUTPUT);
pinMode(LS,INPUT);
pinMode(echo,INPUT);
pinMode(trig,OUTPUT);
//pinMode(A3,OUTPUT);
lcd.begin(16,2);
Serial.begin(9600);
}

## Slide 7
void loop() {
int a,d;
int b= digitalRead(LS);
lcd.setCursor(0,0);
lcd.print("Distance=");
d= getDistance();
Serial.println(d);
Serial.println(b);
lcd.print(d);
delay(500);
lcd.clear();
if(b==0){
if(d<=50){
digitalWrite(l2,HIGH);
delay(5000);
}
}
else{
digitalWrite(l2,LOW);
}
digitalWrite(l1,LOW);
}

## Slide 8
long getDistance() {
digitalWrite(ULTRASONIC_TRIGGER_PIN, LOW);
delay(50);
digitalWrite(ULTRASONIC_TRIGGER_PIN, HIGH);
delay(50);
digitalWrite(ULTRASONIC_TRIGGER_PIN, LOW);
return 0.0347*pulseIn(ULTRASONIC_ECHO_PIN, HIGH) / 2;
}

## Slide 9: Output
The output shows the distance measured by the ultrasonic sensor, the value of the light sensor, and whether or not the alarm pin is activated based on certain conditions. The LCD screen displays the distance value and clears every 500ms, and the LED connected to pin l2 is activated for 5 seconds if the distance is less than or equal to 50 and the light sensor detects darkness.
Sample output-
Distance=29
0
Distance=31
0
Distance=35
0
Distance=40
1
Distance=43
1
Distance=50
1

## Slide 10: Bank Alarm System code
int LIGHT_SENSOR=1;
int ULTRASONIC_TRIGGER_PIN=6;
int ULTRASONIC_ECHO_PIN =7;
int GAS_SENSOR=A0;
int ALARM_PIN=9;
int light_value = 0;
long distance = 0;
int gas_value = 0;
void setup() {
pinMode(LIGHT_SENSOR, INPUT);
pinMode(ULTRASONIC_TRIGGER_PIN, OUTPUT);
pinMode(ULTRASONIC_ECHO_PIN, INPUT);
pinMode(GAS_SENSOR,INPUT);
pinMode(ALARM_PIN, OUTPUT);
digitalWrite(ALARM_PIN, LOW);
Serial.begin(9600);
}

## Slide 11
void loop() {
light_value = analogRead(LIGHT_SENSOR);
distance = getDistance();
gas_value = analogRead(GAS_SENSOR);
if((distance < 20 && gas_value > 250) || (light_value <100 && distance < 20 ) || (gas_value > 250 && light_value <100 )) {
digitalWrite(ALARM_PIN, HIGH);
delay(5000);
digitalWrite(ALARM_PIN, LOW);
delay(1000);
}
Serial.println(distance);
Serial.println(light_value);
Serial.println(gas_value);
delay(100);
}

## Slide 12
long getDistance() {
digitalWrite(ULTRASONIC_TRIGGER_PIN, LOW);
delay(50);
digitalWrite(ULTRASONIC_TRIGGER_PIN, HIGH);
delay(50);
digitalWrite(ULTRASONIC_TRIGGER_PIN, LOW);
return 0.0347*pulseIn(ULTRASONIC_ECHO_PIN, HIGH) / 2;
}

## Slide 13
Output
The output will be the distance measured by the ultrasonic sensor, the value of the light sensor, and the value of the gas sensor, which will be printed to the serial monitor. If certain conditions are met, the alarm will sound for five seconds and then stop for one second before repeating.
Sample output-
89
23
245
91
23
246
89
23
244
91
ALARM triggered!

## Slide 14: Conclusion
In conclusion, the Bank Alarm System and Highway Lights implemented using IoT technology demonstrate the potential of using interconnected devices to enhance security and safety. The Bank Alarm System detects and alerts the authorities in case of a break-in, while the Highway Lights optimize energy consumption and improve road safety. These examples highlight the benefits of IoT technology and its applications in various industries, ranging from finance to transportation.

## Slide 15: Course learning outcome
Familiar with Arduino environment and its applications.
Able to understand Arduino programming with C++.
Able to Design Smart systems applications.
Learn and understand about any new IDE, compiler, and MCU chip in Arduino compatible boards or similar types.